## Slide 1
BNO085 Embedded
Heading Sensor System
STM32F767ZI + FreeRTOS + NMEA 0183 + ROS2 lifecycle driver
Objective
Acquire calibrated magnetic-field data from BNO085
Calculate magnetic heading and reduce fluctuation on STM32
Transmit standard NMEA HDM sentences over UART
Publish ROS2 IMU orientation, TF and diagnostics
Deliverable focus: reliable sensor acquisition, timing validation and ROS2 integration.
Kuartis Embedded Software Homework · 1

## Slide 2
End-to-End System Architecture
From BNO085 calibrated magnetic field to ROS2 orientation and diagnostics.
BNO085
magnetometer
STM32
SPI/SHTP
Calibration
+ heading
Kalman
X/Y filters
NMEA HDM
UART
ROS2
node
NMEA output
$HCHDM,<heading>,M*checksum
Key interfaces
BNO085 communication through SPI and SHTP packets
UART stream uses readable NMEA 0183 HDM format
ROS2 converts heading into yaw quaternion and TF
Kuartis Embedded Software Homework · 2

## Slide 3
Embedded Runtime Architecture
FreeRTOS tasks isolate sensor acquisition from communication output.
Task-level design
SensorTask
BNO085 process + heading
FreeRTOS Queue
HeadingMessage
CommunicationTask
NMEA + UART output
Sensor state machine
STARTUP
WAIT
PRODUCT ID
CALIBRATING
RUNNING
RECOVERY
Timeouts and communication errors trigger recovery and re-initialization.
UART output path
NMEA sentence
TX ring buffer
Interrupt-driven UART
ROS2 serial input
Complete messages are enqueued to avoid partial NMEA frames.
Kuartis Embedded Software Homework · 3

## Slide 4
Heading Calculation & Kalman Filtering
Heading is calculated from calibrated X/Y magnetic components and stabilized before ROS output.
Heading calculation
heading = atan2(Y, X) × 180 / π
if heading < 0° → heading = heading + 360°
The output is a magnetic heading in the 0° to 360° range.
Filtering strategy
Calibrated X
Kalman 1D
Filtered
Heading
Calibrated Y
Kalman 1D
Kalman parameter selection
Measurement noise R
Stationary magnetic-field variance was estimated with Welford algorithm.
Rx = 0.433 µT² · Ry = 0.393 µT²
Process noise Q = 0.25 µT²/s was tuned for smoothness vs responsiveness.
Core update equations
K = P- / (P- + R)
x = x- + K(z - x-)
Kalman gain is recalculated at every update.
Kuartis Embedded Software Homework · 4

## Slide 5
Performance Validation
Embedded timing and ROS2 publish rate were measured separately.
Embedded timing counters
Embedded result: 99-101 ms period, 2 ms peak-to-peak jitter, 10.003 Hz.
ROS2 publish rate
ROS2 result: /imu/data remains at approximately 10 Hz over 849 samples.
Kuartis Embedded Software Homework · 5

## Slide 6
ROS2 Integration Outputs
Lifecycle node publishes standard ROS interfaces and runtime health information.
Diagnostics output
Connection: Connected, frequency: ~10 Hz.
/imu/data message
Heading is represented as a yaw quaternion.
TF output
base_link to imu_link transform exposes yaw.
Kuartis Embedded Software Homework · 6

## Slide 7
Challenges, Improvements & Live Demonstration
The final step validates the complete embedded-to-ROS data path live.
Challenge
Magnetometer data still showed short-term heading fluctuation after calibration.
Cause: measurement noise and environmental magnetic disturbance.
Solution
Apply independent scalar Kalman filters to calibrated X and Y before heading calculation.
R was measured from stationary variance; Q was tuned experimentally.
Improvement
Add tilt compensation to improve heading reliability when the sensor is not level.
A future version can fuse accelerometer/orientation data for compensated heading.
Live demonstration sequence
1
CubeIDE debug
Check calibration_ok and runtime variables.
2
CubeMonitor graph
Compare raw heading and Kalman-filtered heading.
3
ROS2 topics
Show /imu/data content and publish rate.
4
TF + diagnostics
Show yaw transform and connected status.
Kuartis Embedded Software Homework · 7